BASE-SEAL-100-CONCENTRATE

LIQUID SOIL STABILIZER

MATERIAL   SAFETY   DATA   SHEET

Page 1 of 4

Harmonization Tariff Code  -                                                         1   HMIS  Health

Schedule  B:  2839 . 19 . 0000                                                          0   HMIS  Flammability

Item Number:  35260                                                                       0   HMIS  Reactivity

Transportation Class 55                                                                  C   HMIS  Personal Protection                    ************************************************************************************************

MANUFACTURER’S INFORMATION

************************************************************************************************

| MANUFACTURER……………………………………. | BASE-SEAL INTERNATIONAL, INC. 15822 RIVER ROADS DRIVE HOUSTON, TEXAS U.S.A. 77079 |
| --- | --- |
| EMERGENCY TELEPHONE NUMBER …………… | 281-497 7743 |
| DATE PREPARED ……………………………………. | January 1, 2006 |

************************************************************************************************

SECTION I   -   IDENTIFICATION

************************************************************************************************

| COMMON TRADE NAME…………………………… | BASE-SEAL LIQUID SOIL STABILIZER |
| --- | --- |
| CHEMICAL FAMILY………………………………… | Inorganic Proprietary Cohesive Agents |
| CHEMICAL FORMULA……………………………… | Proprietary |
| CAS NUMBER…………………………………………. | Blend |

************************************************************************************************

SECTION II   -   HAZARDOUS INGREDIENTS

************************************************************************************************

HAZARDOUS INGREDIENTS    %                                 TLV  (Units)                            PROD.   CAS #

NONE

************************************************************************************************

SECTION III   -   PHYSICAL AND CHEMICAL CHARACTERISTICS

************************************************************************************************

| BOILING POINT……………………………………….. | < 212 . 0 Degrees (F) |
| --- | --- |
| FREEZING POINT……………………………………… | > 32 . 0 Degrees (F) |
| VAPOR PRESSURE . (mm Hg 70 C ) …………………. | 17 . 5 |
| VAPOR DENSITY……………………………………….. | 0. 6 |
| SOLUBILITY IN WATER………………………………. | 100% |
| APPEARANCE…………………………………………… | Translucent Liquid |
| ODOR. ……………………………………………………. | None to Slightly Chemical Odor |
| GRAVITY @ 60 Degrees (F) : |  |
| SPECIFIC GRAVITY. (water = 1)…………………. | 1. 4 |
| POUNDS / GALLON :……………………………….. | 11. 6 |
| pH . ……………………………………………………….. | 12. 0 |

BASE-SEAL LIQUID SOIL STABILIZER CONCENTRATE

MATERIAL SAFETY DATA SHEET                  Page 2 of 4

************************************************************************************************

SECTION IV   -    FIRE   &   EXPLOSION DATA

************************************************************************************************

| NFPA CODE………………………………………………… | 0 0 0 |
| --- | --- |
| FLASH POINT……………………………………………… | None - Non-Flammable Liquid |
| LOWER FLAME LIMIT…………………………………… | None - Non-Flammable Liquid |
| HIGHER FLAME LIMIT………………………………….. | None - Non-Flammable Liquid |
| EXTINGUISHER MEDIA…………………………………. | Determined by surrounding media. |
|  | Water fog or spray, foam, dry powder |
|  | carbon dioxide (CO2) |
| SPECIAL FIRE FIGHTING |  |
| PROCEDURES……………………………………………… | None - Non-Flammable Liquid |
| FLAMMABLE LIMITS…………………………………… | None - Non-Flammable Liquid |
| AUTO-IGNITION TEMPERATURES…………………… | None - Non-Flammable Liquid |
| UNUSUAL FIRE & EXPLOSIONS |  |
| HAZARDS…………………………………………………… | None - will not burn, will not explode |

************************************************************************************************

SECTION V    -    HEALTH HAZARD DATA

************************************************************************************************

| THRESHOLD LIMIT VALUE……………………………. | None established for this product |
| --- | --- |
| ROUTES OF ENTRY - |  |
| INHALATION……………………………………………. | Possible slight irritant |
| SKIN……………………………………………………….. | Possible slight irritant |
| INGESTION………………………………………………. | Possible slight irritant |
| HEALTH HAZARDS………………………………………. | Possible slight irritation to skin |
|  | and eyes,. Nose and throat. |
| CARCINOGENICITY - |  |
| NTP………………………………………………………… | No |
| IARC………………………………………………………. | No |
| OSHA REGULATED…………………………………….. | No |
| OVER EXPOSURE EFFECTS……………………………. | Inhalation of vapor or mist may irritate eyes, nose |
|  | and throat. |
| FIRST AID PROCEDURE - |  |
| EYE CONTACT…………………………………………. | Flush immediately with large amounts of water for |
|  | at least 15 minutes. Get medical attention. |
| SKIN CONTACT………………………………………… | Wash affected area thoroughly with soap and water. |
| INHALATION…………………………………………… | Move to fresh air. |
| INGESTION……………………………………………… | DO NOT induce vomiting. Get medical attention |

BASE-SEAL LIQUID SOIL STABILIZER CONCENTRATE

MATERIAL   SAFETY   DATA   SHEET

Page 3 of 4

*******************************************************************************************************************

SECTION VI      -     REACTIVITY DATA

*******************************************************************************************************************

| CHEMICAL STABILITY…………………………………… | Stable |
| --- | --- |
| CONDITIONS TO AVOID………………………………….. | None |
| INCOMPATIBLE MATERIALS…………………………… | Acids, salts and alcohols. DO NOT STORE |
|  | ALUMINUM CONTAINERS. |
| DECOMPOSITION PRODUCTS…………………………… | None |
| POLYMERIZATION TO AVOID………………………….. | None |

************************************************************************************************

SECTION  VII   -   SPILL  OR  LEAK  PROCEDURE

************************************************************************************************

| SPILL………………………………………………………….. | Absorb with inert material. |
| --- | --- |
| LEAK………………………………………………………….. | Absorb with inert material. |
| DISPOSAL METHODS……………………………………… | Follow state regulations for non-hazardous |
|  | materials. |

DO NOT STORE IN ALUMINUM CONTAINERS

************************************************************************************************

SECTION   VIII   -   SPECIAL PROTECTION

************************************************************************************************

| RESPIRATORY PROTECTION - |  |
| --- | --- |
| OPEN AIR……………………………………………….. | None |
| INSIDE / CONFINED SPACES………………………. | NIOSH Approved vapor / mist protection. |
| VENTILATION……………………………………………….. | Local exhaust |
| MECHANICAL EXHAUST………………………………….. | Recommended inside building or in confined space. |
| PROTECTIVE GLOVES…………………………………….. | Recommended |
| OTHER PROTECTIVE EQUIPMENT…………………….. | HMIS Personal Protection: “C” safety glasses, |
|  | gloves, apron |

************************************************************************************************

SECTION IX   -   SPECIAL HANDLING

************************************************************************************************

| HANDLING AND STORAGE……………………………….. | Protect from temperatures above 120 degrees (F) or |
| --- | --- |
|  | below 32 degrees (F). |
| PRECAUTIONARY MEASURES…………………………… | Provide fresh air ventilation during and after |
|  | application. Close container after each use. |

BASE-SEAL INTERNATIONAL CONCENTRATE

MATERIAL   SAFETY   DATA   SHEET

Page 4 of 4 ************************************************************************************************

SECTION IX   -   SPECIAL HANDLING, ( CON’D)

************************************************************************************************

| PRECAUTIONARY MEASURES…………………………… | Avoid prolonged or repeated contact with skin. |
| --- | --- |
|  | Avoid contact with the eyes. After handling, |
|  | wash hands before eating or drinking. |
| HAZARDOUS CLASS………………………………………… | Non Regulated |
| DOT SHIPPING NAME……………………………………… | ROADMASTER BASE LIQUID SOIL |
|  | STABILIZER. |
| REPORTABLE QUANITITY….(RQ)………………………. | None |
| UN NUMBER………………………………………………….. | None |
| NA #……………………………………………………………. | None |
| PACKAGING SIZES…………………………………………. | 55 Gallon Drums, Bulk |

************************************************************************************************SECTION X   -    REGULATORY INFORMATION

************************************************************************************************

| EPA ACUTE…………………………………………………… | Acute (eyes) |
| --- | --- |
| EPA CHRONIC……………………………………………….. | No |
| EPA IGNITABILITY…………………………………………. | No |
| EPA REACTIVITY…………………………………………… | No |
| EPA SUDDEN RELEASE OF PRESSURE…………………. | No |
| EPA HAZARD WASTE NUMBER………………………….. | None |
| CLEAN AIR…………………………………………………… | N/A |
| CLEAN WATER……………………………………………… | N/A |
| CERCLA RQ VALUE………………………………………… | None |
| SARA TPQ…………………………………………………….. | None |
| SARA RQ………………………………………………………. | None |
| SECTION 313…………………………………………………. | No |

************************************************************************************************

THE PRODUCT DATA AND SAFETY INFORMATION PRESENTED ABOVE IS PROVIDED TO ASSIST OUR CUSTOMERS IN ASSESSING COMPLIANCE WITH HEALTH, SAFETY AND ENVIRONMENTAL REGULATIONS.  THE INFORMATION CONTAINED HEREIN IS BASED ON DATA AVAILABLE TO THE MANUFACTURER AND IS BELIEVED TO BE COMPLETE AND ACCURATE.

THE APPLICATION OF THIS PRODUCT IS UNDER THE EXCLUSIVE CONTROL OF THE END-USER.   IT IS THE OBLIGATION OF THE END-USER TO DETERMINE THAT THE CONDITIONS

ARE SAFE FOR THE UTILIZATION OF THIS PRODUCT.