## TOP-SHIELD LIQUID SOIL SEALANT

MATERIAL SAFETY DATA SHEET

## Harmonized Tariff Code - 					1	HMIS Health

## Schedule B: 3906.10.000					0	HMIS Flammability

## Item Number: 46030					0	HMIS Reactivity

Transportation Class: 55					C	HMIS Personal Protection

SUPPLIER’S INFORMATION

SUPPLIER:					BASE SEAL INTERNATIONAL, INC.

15822 River Roads

Houston, TX  77079

(281) 497-7743

DATE PREPARED:				June 12, 1996

SECTION I – IDENTIFICATION

### COMMON TRADE NAME:					TOP-SHIELD Liquid Soil Sealant

CHEMICAL FAMILY:					Copolymer Emulsion

CHEMICAL FORMULA:					Proprietary

CAS REGISTRY NUMBER:				Not Assigned

SECTION II – INGREDIENTS

|  |  | OSHA | ACGIH |  |
| --- | --- | --- | --- | --- |
| COMPONENTS | % | TWA | STEL | TVL | STEL | CAS REG. # |
| Proprietary Copolymer | 50% | NONE | NONE | NONE | NONE | NON-HAZARDOUS |

SECTION III – PHYSICAL AND CHEMICAL CHARACTERISTICS

BOILING POINT				212.0 degrees (F)

FREEZING POINT				32.0 degrees (F)

VAPOR PRESSURE			17.5 mm Hg

SOLUBILITY IN WATER			Dilutable

APPEARANCE				Milky White Liquid

ODOR					Characteristically acrylic odor

SPECIFIC GRAVITY			1.01-1.15

Ph						5.5

VOLATILE ORGANIC CONTENT		0

TOP-SHIELD LIQUID SOIL SEALANT

MATERIAL SAFETY DATA SHEET

SECTION IV – FIRE & EXPLOSION DATA

NFPA CODE					000

FLASH POINT				None – Non Flammable Liquid

LOWER FLAME LIMIT			None – Non Flammable Liquid

HIGHER FLAME LIMIT			None – Non Flammable Liquid

EXTINGUISHER MEDIA			Determined by surrounding media.

Water fog or spray, foam, dry powder,

Carbon dioxide (CO2)

SPECIAL FIRE FIGHTING

PROCEDURES				None – Non Flammable Liquid

FLAMMABLE LIMITS			None – Non Flammable Liquid

AUTO-IGNITION TEMPERATURE	None – Non Flammable Liquid

UNUSUAL FIRE & EXPLOSION

HAZARDS					May splatter above 212 degrees (F)

Polymer film can burn but will not

Support combustion.

SECTION V – HEALTH HAZARD DATA

THRESHOLD LIMIT VALUE		None established for this product

ROUTES OF ENTRY –

INHALATION			Irritant

SKIN					Possible irritant

INGESTION				Irritant

HEALTH HAZARDS			Irritating to skin and eyes. Vapor from undiluted

Material can cause headache and / or nausea.

CARCINOGENICITY –

NTP					No

IARC MONOGRAPHS		No

OSHA REGULATED		No

OVER EXPOSURE EFFECTS 	Inhalation of vapor or mist can cause the   following:headache, nausea irritation of nose, throat and lungs.

FIRST AID PROCEDURES –

EYE CONTACT	Flush immediately with large amounts of water for at least 15 minutes. Get medical attention.

SKIN CONTACT	Wash affected area thoroughly with soap and water

INHALATION			Move to fresh air

INGESTION				DO NOT induce vomiting. Get medical

attention.

TOP-SHIELD LIQUID SOIL SEALANT

MATERIAL SAFETY DATA SHEET

SECTION VI – REACTIVITY DATA

CHEMICAL STABILITY			Stable

CONDITIONS TO AVOID			None

INCOMPATIBLE MATERIALS		None

DECOMPOSITION PRODUCTS		From Fire: smoke, carbon dioxide (CO2),

carbon monoxide (CO) and traces of monomer

HAZARDOUS POLYMERIZATION	Will not occur.

POLYMERIZATION TO AVOID		None

CORROSIVE TO METALS			No

OXIDIZER					No

SECTION VII – SPILL OR LEAK PROCEDURES

SPILL / LEAK 				Dike, control and absorb with inert material.

Transfer liquid to containers for recovery /

disposal. DO NOT ALLOW SPILLED OR

LEAKED MATERIAL TO FLOW INTO PUBLIC

SEWERS OR OPEN BODIES OF WATER.

DISPOSAL METHOD			Coagulate the emulsion by the stepwise

addition of ferric chloride and lime. Remove the

clear supernatant liquid and transfer to appoved chemical sewer or landfill.  Follow state regulations for non-hazardous materials.

CONTAINER DISPOSAL			Do not re-use containers. Do not weld on

Metal containers

SECTION VIII – SPECIAL PROTECTION

RESPIRATORY PROTECTION –

OPEN AIR				None

INSIDE/CONFINED SPACE	NIOSH Approved vapor/mist protection

VENTILATION			Local exhaust

MECHANICAL EXHAUST		Recommended inside building or in

confined space.

PROTECTIVE GLOVES		impervious type recommended.

SAFETY GLASSES			Recommended

OTHER PROTECTIVE

EQUIPMENT				HMIS Personal Protection: ”C” safety glasses,

gloves, apron. Risk of exposure to residual

monomer is negligible.

TOP-SHIELD LIQUID SOIL SEALANT

MATERIAL SAFETY DATA SHEET

SECTION IX – SPECIAL HANDLING

HANDLING AND STORAGE	Store in shady or protected areas where the temperatures are below 112 degrees (F) or above 32 degrees (F).

PRECAUTIONARY MEASURES	Provide fresh air ventilation during and after

application. Close container after each use.

Avoid prolong or repeated contact with skin.

Avoid contact with eyes. After handling, wash

hands before eating and drinking.

HAZARD CLASS				Non-regulated

DOT SHIPPING NAME			TOP-SHIELD Liquid Soil Sealant

REPORTABLE QUANTITY (RQ)		None

UN NUMBER				None

NA #						None

PACKAGING SIZES			5 gallon pail, 55 gallon drum, bulk

SECTION X – REGULATORY INFORMATION

EPA ACUTE					Yes (eyes)

EPA CHRONIC				No

EPA IGNITABILITY				No

EPA REACTIVITY				No

EPA SUDDEN RELEASE OF

PRESSURE					No

EPA HAZARD WASTE NUMBER		None

CLEAN AIR					N/A

CLEAN WATER				N/A

CERCLA RQ VALUE			None

SARA TPQ					None

SARA RQ					None

SARA SECTION 313

“CONTROLLED MATERIAL” –

WHMIS   (Canada)				No

THE PRODUCT DATA AND SAFETY INFORMATION PRESENTED ABOVE IS PROVIDED TO ASSIST OUR CUSTOMERS IN ASSESSING COMPLIANCE WITH HEALTH, SAFETY AND ENVIRONMENTAL REGULATIONS.

THE INFORMATION CONTAINED HEREIN IS BASED ON DATA AVAILABLE TO THE MANUFACTURER AND IS BELIEVED TO BE BOTH COMPLETE AND ACCURATE.